# Precision pressure maintenance 
Simply Compresso C 2.1 – 80 S

Precision pressure maintenance, +/-0.1 bar, with compressor for heating, solar and cooling water systems, and systems according to EN 12828, EN 12976, SWKI 93-1, ENV 12977.

Antifreeze additive up to 50%.

TecBox control unit, space-saving mounting together with the base vessel 80 litres.

Compact unit pre-mounted with all necessary functional elements, high-quality metal chassis including air-side connection with the base vessel.  Extension vessel with 80 l content easy to mount.

Plug & Play installation and start-up. Getting the Simply Compresso up and running only takes three easy steps.

Pressure maintenance with ECO-night mode. Keeping compressor runtime to the absolute minimum

Silent run operation, particularly low-noise, noise level 59 dB(A)

Pressure optimized starting mode, 1 compressor, 1 overflow valve.

Check of the amount, time, frequency and a decalcification unit Pleno refill.

BrainCube Connect control for intelligent and safe plant operation, self-optimizing memory and data storage, self-explanatory, operation-oriented menu, help texts and clear text communications.

Easy to use illuminated 3.5 "color TFT touch-screen display for presentation of all relevant parameters, data, and graphics.

Ethernet interface to connect to the Internet and remote access.

All data via Internet access read- and changeable.

Alarm message via Internet or transfer to BMS system.

USB and RS485 interface with Modbus communication.

2 potential-free, individually configurable digital outputs, numerical and graphical display of pressure and content.

Electrical connection with special coupling to the mains, CE-marked according to the requirements of the European directives PED/DEP 97/23/EC, 2004/108/EC, 2006/95/EC.

Swiss made by Pneumatex.

Max. Temperature		70°C

Min. Temperature		5°C

Voltage:			230 V / 50/60 Hz.

Power 				0.3 kW

Producer:			IMI-Pneumatex

Type:				Simply Compresso C 2.1-80 S

Max. Pressure 			3 bar

Art.-No:               		30102141001