# Automatic dirt separator Zeparo G-Force SG 
DN 65-300 PN16

Version Dirt, Cyclone design, for heating and cooling water systems.

Antifreeze additive up to 50%.

Unique cyclone technology with up to 9 times better separation performance than conventional systems.

Separation of particles with a minimum size of 5µm.

Efficiency increases with increasing flow rate.

No clogging as with filters. Secluded dirt is collected and separated in the separation chamber.

Prepared to mount a magnetic rod.

Horizontal and vertical mounting.

Desludging valve with cap for connecting a hose can be mounted in 4 positions

Connections:		Welding and grooved ends

Housing: 		Steel. Colour beryllium

Max. Pressure: 		16 bar

Max. Temperature: 	110°C

Min. Temperature:	-10°C

Producer:		IMI Pneumatex

Type:			Zeparo G-Force SG DN 65 PN16

Art. No.                	313 4124 1000

Type:			Zeparo G-Force SG DN 80 PN16

Art. No.                	313 4124 1100

Type:			Zeparo G-Force SG DN 100 PN16

Art. No.                	313 4124 1200

Type:			Zeparo G-Force SG DN 125 PN16

Art. No.                	313 4124 1300

Type:			Zeparo G-Force SG DN 150 PN16

Art. No.                	313 4124 1400

Type:			Zeparo G-Force SG DN 200 PN16

Art. No.                	313 4124 1500

Type:			Zeparo G-Force SG DN 250 PN16

Art. No.                	313 4124 1600

Type:			Zeparo G-Force SG DN 300 PN16

Art. No.                	313 4124 1700